Gun_PID

Purpose: Controls PID for the gun

Public functions:

GunSpeed – Takes user input to set Target GunSpeed, which the PID matches

GetGunSpeed – retrieves the current GunSpeed

Interrupt _Vec_tim1ch4 Gun_Encoder

Purpose: Gets encoder ticks and calculates a period from the gun wheel rotation

Inputs: None

Return Value: None

Declare LastEdge=0 as a static

Set NewEdge to the current value of the timer

EncodePeriod = NewEdge - LastEdge;

LastEdge = NewEdge;

EnableInterrupts;

Clear the flag

Interrupt Gun_SpeedControl

Purpose: Calculates New PWM to control speed of the gun wheel

Inputs: None

Return Value: None

Declare Integral=0 as a static variable

Reset Timer

Clear the timer flag

EnableInterrupts, b/c We don't want to miss encoder ticks

Period = EncodePeriod;

Speed = constant/Period;

Error = Target_Speed - Speed;

Integral += Error;

DutyCycle = (Error * _Kp_ + Integral * _Ki_);

if(DutyCycle > FULL_GUN_DUTY)

DutyCycle = FULL_GUN_DUTY, b/c Duty cycle can't be more than max value

Integral -= Error, to Unwind the overshoot

if(DutyCycle < 0)

DutyCycle = FULL_GUN_DUTY, b/c Duty cycle can't be less than 0

Integral -= Error, to Unwind the overshoot

Set the Duty Cycle

GunSpeed

Purpose: Sets gun Speed for PID control interrupt

Inputs: Target

Return Value: None

Target_Speed = Target;

GetGunSpeed

Purpose: Calculates New PWM to control speed of the gun wheel

Inputs: Distance

Return Value: Speed to set gun

CurrentTarget = GetTarget();

TargetLocation = GetTargetLocation(CurrentTarget);

DeltaX = x coord of TargetLocation - Current x coord

DeltaY = y coord of TargetLocation - Current y coord

Distance = sqrt(DeltaX*DeltaX + DeltaY*DeltaY);

//Map Speed every 2 inches

return corresponding speed