Gun

Purpose: Performs all basic actions for

Public functions:

Release_Ball – Releases a ball onto the already spinning wheel (firing the ball)

Gun_Motor_Init

Description: Initializes all the ports associated with the Gun System to INPUTS

or OUTPUTS.  Initializes the PWM subsystem or the Gun System.

Parameters:  None

Returns:  None

PseudoCode

Initialize the S12Timer Module

Set Bit to output for Gate #2

Set Bit to output for Gate #1

Gate_1_Open

Description:    Sets Gate1 bit HI in order to open the door lock

Parameters:  None.

Returns:  None.

Pseudo-Code:

Set Gate1 Bit HI

Set PWM to midrange value

Gate_1_Closed

Parameters:     None.

Returns:     None.

Description:     Sets Gate1 bit LO in order to close the door lock

Pseudo-Code:

Set Bit 3 of Port P LO

Set PWM to 0

Gate_2_Open (top gate)

Parameters:    None.

Returns:     None.

Description:  Sets Gate1 bit HI in order to open the door lock

Pseudo-Code:

Set Gate2 Bit HI

Set PWM to moderate-low value (30-40%)

Gate_2_Closed

Parameters: None.

Returns:     None.

Description:  Sets Gate1 bit LO in order to close the door lock

Pseudo-Code:

Set Gate2 Bit LO

Set PWM to 0

Release_Ball

Parameters:     None.

Returns:     None.

Description

Controls the OPEN/CLOSE sequence of the door locks to release one ball

Pseudo-code:

Open gate 1

SetTimer for 300ms

while(timer hasn't expired yet)

//Wait

Clear the timer flag

Gate_1_Reset();

Close Gate #1

SetTimer for 300ms

while(timer hasn't expired yet)

//Wait

Clear the timer flag

Reset Gate #1

Open gate #2

SetTimer for 300ms

while(timer hasn't expired yet)

//Wait

Clear the timer flag

Reset Gate #2

Close Gate #2

SetTimer for 300ms

while(timer hasn't expired yet)

//Wait

Clear the timer flag

Reset Gate #2

Balls_Left = Balls_Left -1; // reduce ball count by 1