SPI

Purpose: Initializes and Handles Serial Communications with Target Commander

Public functions:

SPIM_InitializeSPI – Initializes SPI interface

Request_IR_Illumination – Asks target commander to illuminate IR selected IR beacon

Query_Current_Target – Asks commander to return current target

ResponseDecoder – Decodes Hex input from target commader, converting to enumerated event_t

SPIM_InitializeSPI

Parameters: None.

Returns:   None.

Description: Initializes SPI mode and transfer rate

Pseudo-Code:

Initialize Baud Rate to 12.21kHz

Initialize Clock to Mode 3

Set as Master

Enable Slave Select

Enable SPI Interupts

Make sure normal mode is enabled

Enable SPI

EnableInterrupts

SPI_Transmit_And_Receive

Parameters:   A number representing a specific command.

Returns:     A number representing a specifc response to the command

Description: Performs data tranfer with Target Commander

Pseudo-code:

READ RECEIVE REGISTER

Wait for byte to be transfered

Once the data transmitting is complete, write SPIDR data register with QueryData

WRITE SEND REGISTER

Wait for byte to be received

Once the data receiving is complete, read SPIDR data register

READ RECEIVE REGISTER

Wait for byte to be transfered

Once the data transmitting is complete, write SPIDR data register with 0xFF

Wait for byte to be received

Once the data receiving is complete, read SPIDR data register

Return the data received

Query_Current_Target

Parameters: None.

Returns:

Response from Target Commander in number form.  See the TC info sheet

for meaning. If the bot sent and invalid command it will return 0

indicating failure.

Description

To query the Target Commander, a byte of 0xAA is sent to the Target

Commander. The Target Commander will process the query and during

the second byte of the exchange return 0xCx, where x is the number

of the currently active target.

Pseudo-Code:

set receive = SPI_Transmit and Receive, passing 0xAA

return receive

Request_IR_Illumination

Parameters

Give the function the number which represents the beacon you want to

illuminate (see TC info sheet).

Returns

Response from Target Commander in number form.  See the TC info sheet

for meaning. If the bot sent and invalid command it will return 0

indicating failure.

Description

To request that the Target Commander illuminate a specific Goal

beacon, send a byte of 0xEx to the Target Commander, replacing ?x?

with the number of the Goal beacon to be illuminated. The Target

Commander will immediately reply with 0xFB, indicating that the

request has been forwarded to the field and the TC is busy waiting

for the field?s reply. Repeated Enable IR commands will be responded

to with 0xFB until the field responds to the TC. Once the Target

Commander receives confirmation from the field, the TC will respond

to the next Enable IR command with the current status of the

requested beacon (0x4x ? 0x7x). Between the time that an Enable

IR command has been received and the beacon status is returned by

the field, a Beacon Status command may not be issued. If a Beacon

Status command is received during this time, the TC will respond

with 0xEx.

Pseudo-Code:

switch statement cataloguing possible return values ( input beacon number, output 0xE[beacon#_in_hex] )

Send hex-code to Targer commander using SPI_Transmit_And_Receive

set return value to Receive

return Recieve

ResponseDecoder

Purpose: Convert hex reponses into easily interpretted enumerated types Event_t

Parse the FirstWord (4 bits)

Parse the SecondWord (4 bits)

// Filter out the responses

switch (FirstWord)

case (0xC0):

return EV_RECIEVED_TARGET;

case (0x40):

return EV_BEACON_INNACTIVE;

case (0x50):

return EV_BEACON_ACTIVE_NOT_ILLUM;

case (0x60):

return EV_BEACON_ACTIVE_ILLUM;

case (0x70):

return EV_BEACON_HIT;

case (0x80):

return EV_BEACON_HIT; //Duplicates case 0x70

case (0xD0):

switch (SecondWord)

case (0x0E):

return EV_GAME_NOT_STARTED;

case (0x0A):

return EV_RETURN_HOME;

case (0x0D):

return EV_GAME_OVER_RED_WINS;

case (0x0C):

return EV_GAME_OVER_GREEN_WINS;

case (0xF0):

switch (SecondWord)

case (0x0F):

return EV_OFFLINE;

case (0x0B):

return EV_COMMANDER_BUSY;

case (0x0E):

return;

case (0xB0):

return;

case (0xE0):

return;

default:

return;